## Slide 1
CLICK SENSOR HUB
THE TEAM:
ALFONSO DE LA MORENA <PM>, DYLAN DEAN, MOHAMED SGHARI
SPONSOR: DR KEVIN KEMP <NXP>
FACULTY ADVISOR: DR WILLIAM STAPLETON

## Slide 2
Click boards are plug-and-play modules designed to add extra functionality to existing development kits. These small, function-specific add-on boards/modules all have a common interface to the mikroBUS; adapter board.
What are Clicks?

## Slide 3
Why use Clicks?
Major chip vendors are endorsing it
It's an open standard
mikroBUS™ - the add-on board standard that offers maximum expandability with the smallest number of pins. Integrate it into your design and open the doors of thousands of possibilities.

## Slide 4
What is the Click Sensor Hub?
# | Project Requirements
1 | PCB that connects FRDM-KL46Z to 4 mikroBUS Sockets
2 | Each of the 4 sockets receive 5V and 3.3V channels
3 | Each of the 4 sockets must communicate with SPI, UART, PWM, I2C and Analog
4 | Write code to test at least 10 Clicks on the Board

## Slide 5
NXP Hexiwear:
Hexiwear Docking Station
Project Motivation
NXP FRDM-KL46Z Board:
Click Sensor Hub
Notes: Why did we start this project? An attempt to Improve and expand upon current click SHIELD, and provide the microprocessors course at Texas State with an IoT development kit.

## Slide 6
Hardware Approach

## Slide 7
Hardware – First Board Design
Pros
More space for clicks
Cons
Complicated wiring
Cost more

## Slide 8
Hardware – Second Board Design
Pros
Smaller board size
Shorter wire connection
Four Sockets all have SPI, UART, I2C, PWM and Analog
Cons
Soldering ICs difficult with available equipment

## Slide 9
Hardware – Third Board Design
Pros
Cost less
Easier to code
Cons
Only one Socket has UART protocol connection

## Slide 10
Software Approach

## Slide 11
How to deal with multiple sockets

## Slide 12
Pull-Up Network
Example of I2C Click Approach

## Slide 13
Example of SPI Click Approach

## Slide 14
Examples of Click Validation
Test Case | Test Specifications | Test Results | Compliance
Light Ranger 3 Click | Board powered by 3.3V connection | Connected board and checked LED light | Pass
 | Ensure safe connection to FRDM-KL46Z, no feedback voltage should be above 3.3V | Voltages of respective pins measured to be below 3.3V threshold | Pass
 | Get distance readings from Click | Non-zero reading recorded and displayed on PUTTY | Pass
Test Case | Test Specifications | Test Results | Compliance
Bar Graph 2 Click | Board powered by 3.3V and 5V connections | Connected board and checked LED light | Pass
 | Ensure safe connection to FRDM-KL46Z, no feedback voltage should be above 3.3V | Voltages of respective pins measured to be below 3.3V threshold | Pass
 | Cycle Bar Graph Click through set pattern | Pattern set and displayed on Click | Pass
Notes: PRINT FULL SHEET OF CLICK VALIDATION TEST CASES AND BRING 4 COPIES FOR FDR

## Slide 15
Example of Board/Socket Validation
Test Cases | Test Specifications | Test Results | Compliance
Socket #1 |  |  | Passed 5/5
(AN) Analog | Test Analog Click on Socket | Putty output achieved on selected socket with Air Quality Click | Pass
(MISO/MOSI) (CS/SCK) SPI | Test SPI Click on Socket | Bar Graph Click had selected pattern displayed on selected socket | Pass
(RX/TX) UART | Test UART Click on Socket | Serial connection on computer via selected socket | Pass
(SCL/SDA) I2C | Test I2C Click on Socket | I2C connection displayed data on PUTTY terminal using Temp2Hum Click via the selected socket | Pass
PWM | Test PWM Click on Socket | Bar Graph Click had selected pattern displayed on selected socket | Pass
(+3.3V/+5V) VCC/GND | All four mikroBUS™ sockets have both an optional 3.3V and 5V channel. All four mikroBUS™ sockets are grounded | When PCB is powered with 10v and 1amp. Both the +3.3V and +5V channels display proper voltage output. The GND has 0V output | Pass

## Slide 16
Final Results
# | Objective | Result of Requirements | Status
1 | Create a board that connects 1 FRDM-KL46Z to 4 MikroBUS standard sockets | All tests passed | Pass
2 | Write necessary code for 10 different Clicks to interact with FRDM-KL46Z via the board created in the first objective | 7/10 tests passed | Partial
3 | Power 4 simultaneous MikroBUS standard sockets via 3.3V and 5V channels provided by a power source that takes 10V/1A | All tests passed | Pass
4 | Create a user guide that details how to implement and make changes to the project | All tests passed | Pass
5 | Stretch Goal – Create cloud hosted website that compiles all the necessary project information in one place. | All tests passed | Pass

## Slide 17
Click Results
CLICK NAME | Description and Interface | Interface | Requirement | Status
USB UART 3 click | Adds USB 2.0 functionality | UART | Detect serial connection in PC | Fail
Color 5 click | Integrated color sensing device | I2C | Non-Zero Putty output reading | Fail
BarGraph 2 click | 10-segment bar graph display click, which uses a high-quality, multicolor bar graph LED display | PWM & SPI | Pattern displayed on bar graph | Pass
Accel 5 click | Triaxial accelerometer sensor | I2C & SPI | Non-Zero Putty output reading | Fail
Gaussmeter click | Gaussmeter used for measuring the magnetic field in X, Y and Z axes | I2C & SPI | Non-Zero Putty output reading | Pass
LightRanger 3 click | Accurate distance measurement based on a ToF (Time of Flight) measurement principle | I2C | Non-Zero Putty output reading | Pass
Alcohol click | Portable alcohol detector, breathalyzer for estimating BAC | Analog | Non-Zero Putty output reading | Pass
Air Quality click | detecting a variety of gases that impact air quality in homes and offices | Analog | Non-Zero Putty output reading | Pass
microSD click | A microSD card slot for microSD cards used as a mass storage media for portable devices | SPI | Read SD card file via board | Pass

## Slide 18
Acknowledgements