## Slide 1
Sponsor: Dr. Kevin Kemp, NXP
Faculty Advisor: Dr. William Stapleton, TXST
Team Members (Left to Right) : Dylan Dean, Alfonso de la Morena [PM], and Mohamed Sghari
#2.8 CLICK SENSOR HUB
Notes: Pitch
The PM starts the presentation then turns it over to others who speak in turn
Each person should introduce themselves and speak to the design and status of their subsystem
My name is Dylan Dean, I am the Software Engineer and currently…
My name is Alfonso de la Morena, I am the Project Manager and currently…
My name is Mohamed Sghari, I am the Hardware Engineer and currently…

## Slide 2
This is Click Sensor Hub
Notes: What did you design? An extension board for the FRDM-KL46Z Development Board made by NXP
What does it do? Our Board enables the KL46Z to become a full fledge IoT development kit, by providing four MikroBUS sockets that meet industry standardized constraints. As wells as the channels for each type of communication interface.
Why? NEXT SLIDE

## Slide 3
Why design an extension board?
Intel Joule Board:
click SHIELD+
Top Mounted to MCU
Rough Cost - $354.00
Linux Based Beaglebone:
mikroBUS Cape
Top Mounted to MCU
Rough Cost - $71.00
NXP FRDM-KL46Z Board:
click SHIELD
Top Mounted to MCU
Rough Cost - $39.00
NXP FRDM-KL46Z Board:
Click Sensor Hub
Bottom Mounted to MCU
Rough Cost - $50.00
Notes: Why did we start this project? An attempt to Improve and expand upon current click SHIELD, and provide the microprocessors course at Texas State with an IoT development kit.

## Slide 4
Name | Responsibility
Alfonso | Activity and resource planning for meeting deadlines Document Full Functionality Test Mbed code to interfacing between board and sockets Stretch – Front/back end Website Development Stretch – Manage cloud hosting for website
Dylan | Coding to interface between board, clicks, and sockets Presentation/Poster content, User guide, YouTube channel Documenting the Click Validation Test Stretch – Website Designer (CSS/HTML)
Mohamed | PCB Design/Edits in Eagle CAD Documenting the Hardware Functionality Test Soldering prototype boards Stretch – Instructional web articles for hardware usage
Team Roles and Responsibilities
Notes: Brief descriptions – at this point each team member should introduce themselves “My name is … and I am responsible for … “ Paraphrase the description here, do not read word for word.

## Slide 5
# | Functional Deliverable | Status
1 | PCB fits 1 FRDM-KL46Z and 4 Click sensors simultaneously | Completed
2 | Click transmission over SPI | In-progress
3 | Click transmission over IIC | In-progress
4 | Click transmission over PWM | In-progress
5 | Click transmission over UART | In-progress
6 | Click transmission over Analog | In-progress
7 | Signals from 4 sockets transmitted simultaneously | Not started
8 | Example programs for 10 Clicks uploaded to GitHub | Not started
9 | Results from Clicks recorded and graphed | Not started
# | Stretch Goals | Status
1 | Website launched on Google Cloud Services | Completed
2 | Video and PDF tutorial launched on website | Not started
Project Goals

## Slide 6
Product Design
Notes: This is the focus of the presentation
Minimum of 3 /maximum of 12 slides
Use functional block diagrams (what is each block and how does it connect to the other blocks), state diagrams, flow charts, etc. to show your design and describe the operation of your project. Do not write sentences or paragraphs!
Each team member should have 1 to 3 slides.

## Slide 7
Click to add text
Product Design
Old |Design

## Slide 8
New Design
Product Design
3D Model

## Slide 9
Product Design

## Slide 10
Product Design

## Slide 11
Product Design

## Slide 12
Product Design

## Slide 13
Product Design

## Slide 14
Product Design

## Slide 15
# | Major Issues | P.O.A
1 | Board components delayed by Chinese new year | Focused on code/website
2 | Resistors ordered for power component in PCB too small | New order created for larger resistor (size not resistance)
3 | Example code for click sensors not easily available for Mbed platform | Use example code written for ICs that make up the Clicks
4 | Impossible to solder small components with available equipment | New order created for necessary soldering paste
5 | Behind schedule on board testing | Preparing future deliverables while waiting on components
Key Issues
Notes: List the major issues and your plan to resolve.
Do not list – “not enough time”, “too much writing”, etc.

## Slide 16
Upcoming Demo
Notes: List the major issues and your plan to resolve.
Do not list – “not enough time”, “too much writing”, etc.

## Slide 17
Additional Slides for Questions
# | Subject
1 | Service, Support and Maintenance
2 | SPI Connections
3 | Board Layout
4 | Schematic
5 | Shared/Unique Pins
6 | Complete Pinout
7 | Project Selected Clicks
8 | 3D Model

## Slide 18: Service, Support and Maintenance
Maintain a clean board
Use latest software versions
Disconnect from power supply when not in use
Return

## Slide 19
The SPI devices disconnect their MISO pins when they are not selected
Each slave will need a separate SS line
SCK
MOSI
MISO
SS
SCK
MOSI
MISO
SS _ 1
SS _ 2
SS _ n
SLAVE 1
SLAVE 2
SLAVE n
SCK
MOSI
MISO
SS
SCK
MOSI
MISO
SS
Master
Return

## Slide 20
Return

## Slide 21
Return

## Slide 22
Return

## Slide 23: Project Selected Clicks
CLICK NAME | Description and Interface | Interface | Power Supply | Price
Temp&Hum 2 Click | Measures a wide range of temperature and relative humidity values with a great accuracy | I2C | 3.3V | $16.00
USB UART 3 click | Adds USB 2.0 functionality | Serial | 3.3V & 5V | $15.00
Color 5 click | Integrated color sensing device | I2C | 3.3V & 5V | $16.00
BarGraph 2 Click | 10-segment bar graph display click, which uses a high-quality, multicolor bar graph LED display | PWM & SPI | 3.3V | $19.00
Accel 5 click | Triaxial accelerometer sensor | I2C & SPI | 3.3V | $19.00
Gaussmeter click | Gaussmeter used for measuring the magnetic field in X, Y and Z axes | I2C & SPI | 3.3V | $19.00
LightRanger 3 Click | Accurate distance measurement based on a ToF (Time of Flight) measurement principle | I2C | 3.3V | $24.00
Alcohol Click | Portable alcohol detector, breathalyzer for estimating BAC | Analog | 3.3V | $15.00
Air Quality Click | detecting a variety of gases that impact air quality in homes and offices | Analog | 3.3V | $16.50
microSD click | A microSD card slot for microSD cards used as a mass storage media for portable devices | SPI | 3.3V | $16.00
Return