## Slide 1: Challenges
mikroBUS |  | KL-46Z |  | PIN NAME | STATES
Spi | 4 | Spi | 2 | SCK MOSI MISO SS/CS | Shared Shared Shared Unique
I2C | 4 | I2C | 2 | SCL SDA | Shared Unique
Analog | 4 | Analog | 6 | AN | Unique
PWM | 4 | PWM | 6 | PWN | Unique
Interrupts | 4 | Interrupts | 6 | IN | Unique

## Slide 2
Convert
SPI to UART
J1
J2
J3
J4
Power
Input
Voltage Regulator
2 channels 3.3V&5V
Test Point
Test Point
2:4
Decoder 2 to 4
Select Slaves
8:3
Priority Encoder 8 to 3
Interrupter
Reset Button
Reset Button
SS_0
SS_1
SCK_0
MOSI_0
MISO_0
RX_1
TX_1
RX_2
TX_2
RX_4
TX_4
RX_3
TX_3
SS_2
SS_4
CS_2
CS_1
CS_4
CS_3
SCK_1
MISO_1
MOSI_1
AN_1
AN_2
AN_3
AN_4
INT_1
INT_2
INT_3
INT_4
SPI_SC_2
SPI_SC_1
ENCO_1
ENCO_3
ENCO_2
PTA14
PTA6
PTA7
SCL
SDA
R1
R2
PWM_2
PWM_3
PWM_1
PWM_4
SPI
SPI TO UART
I2C
PWM
ANALOG
INTERRUPTER
RESET
GND
v5v
v3v

## Slide 3: SPI: Serial Peripheral Interface
Separate clock and data lines, along with a select line to choose the device you wish to talk to.
Slave
Master
CSCK
MOSI
MISO
SS
GND
CSCK
MOSI
MISO
SS
FRDM KL46Z
Click

## Slide 4
The SPI devices disconnect their MISO pins when they are not selected
Each slave will need a separate SS line
SCK
MOSI
MISO
SS
SCK
MOSI
MISO
SS _ 1
SS _ 2
SS _ n
SLAVE 1
SLAVE 2
SLAVE n
SCK
MOSI
MISO
SS
SCK
MOSI
MISO
SS
Master

## Slide 5: I2C
minimize number of pin and send more that 8 bits data
You can have up to 127 devices on a same bus
R1 and R2 are depended on slave and master voltage
FRDM KL46Z
Clock (SCL)
Data (SDA)
Click
Master
Slaves (n)
R1
R2

## Slide 6
Clock (SCL)
Data (SDA)
R1
R2
Master
Slave 1
Slave 1
Slave n
SCL SDA
SCL SDA
SCL SDA
CLICK 1
CLICK 1
CLICK n

## Slide 7: SC16IS752; SC16IS762 Dual UART with I2C-bus/SPI interface
This chip enables seamless protocol conversion from I2C-bus/SPI to RS-232/RS-485 and is fully bidirectional.
SC16IS752 supports 4 Mbit/s maximum SPI clock speed  SC16IS762 supports 15 Mbit/s maximum SPI clock speed
3.3 V or 2.5 V operation
CTSA: UART clear to send (active LOW), channel A. A logic 0 (LOW) on the CTSA pin indicates the modem or data set is ready to accept transmit data from the SC16IS752/SC16IS762
RTSA: UART request to send (active LOW), channel A. A logic 0 on the RTSA pin indicates the transmitter has data ready and waiting to send

## Slide 8: PWM: Pulse Width Modulation
A series of pulses generate a rectangular waveform which looks something like the following.
Each pulse is characterized by two parameters: period (T) and duty cycle (D)
T may be any length of time
D may be any value in the range 0  D  1
The pulse width is D*T.
Pulse width modulation allows for the automatic generation of a pulse train with specified period and duty cycle/pulse width
T
D*T

## Slide 9: Encoder Logic

## Slide 10: Decoder Logic